## Slide 1: Red and Orange Future Reliability
August 13, 2018
2019 - 2029

## Slide 2: Agenda
Review Future Capacity
Define the Magnitude of Orange and Red Line Changes
Review the controllable and noncontrollable factors that impact current reliability
Present Prediction for Future Orange and Red Line Reliability

## Slide 3: Preface
The Red and Orange Line are complicated networks that operate as a “system of systems” consisting of: Traction Power, Signals, Communications, Vehicles, Operating Rules, Environment, Crew and Customers
Predicting interactions between such complex “system of systems” is challenging given the nearly infinite combination of scenarios and starting conditions.
Reliability predictions utilize system models and expected performance of system components to predict future performance in a defined starting condition.
We have developed a forward looking qualitative reliability prediction utilizing the same tools used for measuring and reporting our performance reliability today.

## Slide 4: Future Capacity
The MBTA is investing in programs to increase the system capacity on the Red and Orange Lines.
  A larger and new fleet of vehicles
  Upgrades to the Signal and Train Control System
  Dwell Time Improvement Initiative
Future Service
  Red Line going to 3 minute peak headways
  Orange Line going to 4.5 minute peak headways

## Slide 5: Capacity vs Reliability
Current Capacity
Future Capacity

## Slide 6: Capacity vs Reliability
The lines are running faster and doing more in the same time period increasing the wear on our system.
The charts below show the weekly wear before and after of both lines.
Increasing a systems wear increases that systems probability of failure.
Chart: Red Line Weekly Current vs Future Wear
| Current | Future
Miles | 45808 | 0 | 53872
Stops | 50153 | 0 | 58656
Trips | 2866 | 0 | 3352
Chart: Orange Line Weekly Current vs Future Wear
| Current | Future
Miles | 23289 | 0 | 26273
Stops | 39930 | 0 | 44934
Trips | 1960 | 0 | 2248

## Slide 7: Orange Line and Red Line Reliability Today
Orange Line
Red Line

## Slide 8: Delay Impact
Detection Time
Trouble Shooting
Recovery
Problem Arises
Back In Service
Taken Out
of Service
Capacity Impacts
Dwell Time Impacts
Longer time a passenger takes to board a train due to crowded platforms or trains. This results in train spending more time at a station
Any incident has cascading impacts on each line.
Cascading Delays can be worse than the initial delay.

## Slide 9: Causes of Delay
Other Factors
Delay
30% Uncontrollable Delays
Police Action
Special Events
Other Factors
70% Controllable Delays
Disabled Train
Signal Problem
Dwell Time
Dwell Time
Uncontrollable Delays will always limit our real service reliability.
Using today’s reporting methods our maximum achievable reliability is 97% & 98% for the Red & Orange lines respectively.

## Slide 10: Controllable Delays
Other Factors
Delay
70% Controllable Delays
Disabled Train
Signals Problem
Dwell Time
Completely New Fleets
Larger Fleet
Better Maintenance Tech
Modern Signal Controls
Upgraded Sections
Better Maintenance Tech
Automatic Train Control Automatic Station Stopping Wider Doors
Improved Procedures

## Slide 11: We expect
Disabled Train
Signals Problem
Dwell Time
Train Related Delays to drop 50-60%
Dwell time related delays will drop by 30-40%
Signals related delays drop by 50-70%
A reliability prediction was conducted considering:
  Improvements to vehicles and infrastructure
  Increased wear on the system due to increased capacity
  Shorter recovery time due to faster headways.

## Slide 12: Reliability Goal
We expect to be able to achieve the following Average Performance Reliability when all vehicles, infrastructure and operational programs are implemented:
We expect hourly, daily weekly and yearly variations based on both controllable and uncontrollable variables
Orange Line
Red Line
Average Reliability 2025
96%
Average Reliability 2025
95%
maximum achievable 98%
maximum achievable 97%

## Slide 13: Next Steps
Development of a 25 year Long Term Asset Management Plan commencing in 2025 to ensure we sustain asset performance
Develop reliability improvement predictions for the line as projects are being completed by 2025
Refine performance calculation beyond current Reliability Metric
Update to Board in January 2019

## Slide 14: Appendix
Additional Information

## Slide 15: Red Line Vehicle and Infrastructure Programs
Signal Design/Build NTP
14 New Cars
Signal Design Underway
Expanded Wellington Yard
62 New Cars
8 Signal Sections Complete
110 New Cars
13 Signal Sections and ATO Complete
186 New Cars
Expanded Codman Yard
Rebuilt Cabot Facility & Yard
252 New Cars
Automatic Train Operation (ATO)
System Tuning
2018
2019
2020
2021
2022
2023
2024
2025
RL Signals Program
Provides early warning diagnostic and maintenance alerts to MBTA Maintenance, reducing failure response time.
RL Infrastructure Program
RL Vehicles Program
Increases fleet size by 16%
All track circuits and 90% of relays will be replaced with electronic microprocessor system, providing redundancy and improved life cycle.
The design considers both reliability and availability.
Improving the Alewife crossover allowing operating speeds through the crossover to increase from 10 mph to 15 mph.
Modern components and systems, which increases reliability.
Decreases the need to immediately remove a car from service and impact to service.
New Test Track
New Testing Shed (allows for static testing/commissioning of the new vehicles without impacting existing maintenance facilities and operations)
Updated Maintenance Facility and Equipment and new Electronics Room (to service the new vehicles and accommodate storage needs)
Upgraded Yard Infrastructure
New Headway Operations

## Slide 16: Improved Orange Line Reliability Due to Vehicle and Signal Programs
2018
2019
2020
2021
2022
2023
2024
2025
6 New Cars
Signal Design/Build NTP
58 New Cars
Signal Design Underway
Expanded Wellington Yard
106 New Cars
Signal Design Underway
Expanded Wellington Facility
152 New Cars
8 Signal Sections & ATO Complete
Rebuilt Wellington Yard
152 New Cars
11 Signal Sections Complete
New Headway Operations
OL Signals Program
Provides early warning diagnostic and maintenance alerts to MBTA Maintenance, reducing failure response time.
OL Infrastructure Program
OL Vehicles Program
Increases fleet size by 27%
All track circuits and 90% of relays will be replaced with electronic microprocessor system, providing redundancy and improved life cycle.
The design considers both reliability and availability.
Updated Maintenance Facility, Facility Equipment and new Electronics Room (to service the new vehicles and accommodate storage needs)
Modern components and systems, which increases reliability.
Decreases the need to immediately remove a car from service and impact to service.
Upgraded Yard Infrastructure
Automatic Train Operations (ATO)
System Tuning